## Slide 1: CS171 Tutorial10 HW5 Cloth Simulation
YiHeng Wu

## Slide 2: -1. HW4

## Slide 3: HW4
Today is 11/30
DDL is 12/2

## Slide 4: 0. Simulation

## Slide 5: Simulation
Hello world
  Start from middle school physics (a is a constant)

## Slide 6: Simulation
Hello world
  Start from middle school physics (a is a constant)
  Calculus (a is a variable)

## Slide 7: Simulation
Hello world
  Start from middle school physics (a is a constant)
  Calculus (a is a variable)
How to solve this ODE?

## Slide 8: Simulation
Hello world
ODE

## Slide 9: Simulation
Hello world
ODE
  Let

## Slide 10: Simulation
Hello world
ODE
  Let
  We get

## Slide 11: Simulation
Hello world
ODE
  Let
  We get
Forward Euler

## Slide 12: Simulation
Hello world
ODE
  Similarly

## Slide 13: Simulation
Hello world
ODE
  Similarly
  Initialize

## Slide 14: Simulation
Hello world
ODE
  Similarly
  Initialize
for (unsigned i = 0; i < 100000; ++i)
Update();

## Slide 15: 1. Mass Spring and Discretization

## Slide 16: Mass Spring and Discretization
Mass
  Divide cloth into masses
    Cloth: 2kg
    Number of masses: 40 * 30 = 1200
    Weight of a mass: (2 / 1200)kg

## Slide 17: Mass Spring and Discretization
Mass
  Divide cloth into masses
    Cloth: 2kg
    Number of masses: 40 * 30 = 1200
    Weight of a mass: (2 / 1200)kg
Spring
  Connect masses with springs

## Slide 18: Mass Spring and Discretization
Mass
  Divide cloth into masses
    Cloth: 2kg
    Number of masses: 40 * 30 = 1200
    Weight of a mass: (2 / 1200)kg
Spring
  Connect masses with springs
Mass spring

## Slide 19: Mass Spring and Discretization
Mass
  Divide cloth into masses
    Cloth: 2kg
    Number of masses: 40 * 30 = 1200
    Weight of a mass: (2 / 1200)kg
Spring
  Connect masses with springs
Mass spring
That is Discretization

## Slide 20: Mass Spring and Discretization
Mass spring
  To solve

## Slide 21: Mass Spring and Discretization
Mass spring
  To solve
  We try to solve it for each mass
    For mass i:

## Slide 22: Mass Spring and Discretization
Mass spring
  To solve
  We try to solve it for each mass
    For mass i:
That is Discretization

## Slide 23: Mass Spring and Discretization
Mass spring
  To solve
  We try to solve it for each mass
    For mass i:
That is Discretization
Status of mass i at t+1
only depends on its status at t

## Slide 24: Mass Spring and Discretization
Mass spring
  To solve
  We try to solve it for each mass
    For mass i:
That is Discretization
Status of mass i at t+1
only depends on its status at t
Explicit!

## Slide 25: Mass Spring and Discretization
Mass spring
  Solve it for each mass

## Slide 26: Mass Spring and Discretization
Mass spring
  Solve it for each mass
  Implementation
for (unsigned i = 0; i < 100000; ++i)
Update();
void Update() {
for (auto& mass : masses) {
Vec3 f = ComputeF();
mass.a = f / mass.m;
mass.v += mass.a * Δt;
mass.x += mass.v * Δt;
}
}

## Slide 27: Mass Spring and Discretization
Mass spring
  Solve it for each mass
  Implementation
for (unsigned i = 0; i < 100000; ++i)
Update();
void Update() {
for (auto& mass : masses) {
Vec3 f = ComputeF();
mass.a = f / mass.m;
mass.v += mass.a * Δt;
mass.x += mass.v * Δt;
}
}
Q1: How to compute f?
Q2: What is Δt?

## Slide 28: 2. Force Computation

## Slide 29: Force Computation
Hooke’s law

## Slide 30: Force Computation
Hooke’s law
  p and q are two masses

## Slide 31: Force Computation
Hooke’s law
  p and q are two masses
A unit vector,
Force direction
Rest length,
“Zero-force length”

## Slide 32: Force Computation
Hooke’s law
Mass Spring Model
  [Xavier Provot 1995]

## Slide 33: Force Computation
Hooke’s law
Mass Spring Model
  [Xavier Provot 1995]
We are ready to compute the force f!

## Slide 34: 3. Fixed Delta Time

## Slide 35: Fixed Delta Time
If you search “fixed delta time” in your browser…

## Slide 36: Fixed Delta Time
Delta time v.s. fixed delta time
  Suppose a = 1, “匀加速直线运动”

## Slide 37: Fixed Delta Time
Delta time v.s. fixed delta time
  Suppose a = 1, “匀加速直线运动”
  Compare:
    Case1: Your program stucks for 10s at the 2nd frame…
    Case2: Your program stucks for 10min at the 2nd frame…
    Are they the same?

## Slide 38: Fixed Delta Time
Delta time v.s. fixed delta time
  Suppose a = 1, “匀加速直线运动”
  Compare:
    Case1: Your program stucks for 10s at the 2nd frame…
    Case2: Your program stucks for 10min at the 2nd frame…
    Are they the same?
Simply let Δt = time of the 2nd frame,
Runs Update() for 1 times at the 3rd frame

## Slide 39: Fixed Delta Time
Delta time v.s. fixed delta time
  Suppose a = 1, “匀加速直线运动”
  Compare:
    Case1: Your program stucks for 10s at the 2nd frame…
    Case2: Your program stucks for 10min at the 2nd frame…
    Are they the same?
  Never!
Simply let Δt = time of the 2nd frame,
Runs Update() for 1 times at the 3rd frame

## Slide 40: Fixed Delta Time
Delta time v.s. fixed delta time
  Suppose a = 1, “匀加速直线运动”
  Compare:
    Case1: Your program stucks for 10s at the 2nd frame…
    Case2: Your program stucks for 10min at the 2nd frame…
Let Δt = 0.02s,
Runs Update() for 500 times at the 3rd frame
Let Δt = 0.02s,
Runs Update() for 5000 times at the 3rd frame

## Slide 41: Fixed Delta Time
Delta time v.s. fixed delta time
  Suppose a = 1, “匀加速直线运动”
  Compare:
    Case1: Your program stucks for 10s at the 2nd frame…
    Case2: Your program stucks for 10min at the 2nd frame…
Let Δt = 0.02s,
Runs Update() for 500 times at the 3rd frame
Let Δt = 0.02s,
Runs Update() for 5000 times at the 3rd frame
Time::fixed_update_time
= 0.02

## Slide 42: Fixed Delta Time
Delta time v.s. fixed delta time
  Time::fixed_delta_time = 0.02
Now we are ready
for (unsigned i = 0; i < 100000; ++i)
FixedUpdate();
void FixedUpdate() {
for (auto& mass : masses) {
Vec3 f = ComputeF();
mass.a = f / mass.m;
mass.v += mass.a * 0.02f;
mass.x += mass.v * 0.02f;
}
}

## Slide 43: Fixed Delta Time
Delta time v.s. fixed delta time
  Time::fixed_delta_time = 0.02
Now we are ready
for (unsigned i = 0; i < 100000; ++i)
FixedUpdate();
void FixedUpdate() {
for (auto& mass : masses) {
Vec3 f = ComputeF();
mass.a = f / mass.m;
mass.v += mass.a * 0.02f;
mass.x += mass.v * 0.02f;
}
}
Have to be done
in world coordinate!!!

## Slide 44: Fixed Delta Time
Delta time v.s. fixed delta time
  Time::fixed_delta_time = 0.02
Now we are ready
  But 0.02 maybe still large…
  We may use 0.001 for HW5…
for (unsigned i = 0; i < 100000; ++i)
FixedUpdate();
void FixedUpdate() {
for (auto& mass : masses) {
Vec3 f = ComputeF();
mass.a = f / mass.m;
mass.v += mass.a * 0.02f;
mass.x += mass.v * 0.02f;
}
}
Have to be done
in world coordinate!!!

## Slide 45: Fixed Delta Time
Delta time v.s. fixed delta time
  Time::fixed_delta_time = 0.02
Now we are ready
  But 0.02 maybe still large…
  We may use 0.001 for HW5…
Only 1 week, QAQ…
So you only need to
implement this function.
for (unsigned i = 0; i < 100000; ++i)
FixedUpdate();
void FixedUpdate() {
for (auto& mass : masses) {
Vec3 f = ComputeF();
mass.a = f / mass.m;
mass.v += mass.a * 0.02f;
mass.x += mass.v * 0.02f;
}
}
Have to be done
in world coordinate!!!

## Slide 46: 4. Framework

## Slide 47: Framework
Run the code
MUST
Optional

## Slide 48: Framework
Run the code
Source
Implement a simple mass spring system here
See how cubes, spheres are generated here
You may find it helpful

## Slide 49: Framework
Run the code
Source
Results

## Slide 50: Framework
Run the code
Source
Results

## Slide 51: Framework
Run the code
Source
Results

## Slide 52: Thank You