## Slide 1: 2. Transmission Lines
7e Applied EM by Ulaby and Ravaioli

## Slide 2: Chapter 2 Overview

## Slide 3: What are Transmission Lines
All structures and media that serve to transfer energy or information between two points, including nerve fibers in the human body and fluids and solids that support the propagation of mechanical pressure waves
We only focus on transmission lines that guide electromagnetic signals. Such transmission lines include telephone wires, coaxial cables carrying audio and video information to TV sets or digital data to computer monitors, microstrips printed on microwave circuit boards, and optical fibers carrying light waves for the transmission of data at very high rates

## Slide 4: Transmission Line is Two-Port Network
A transmission line connects a generator to a load
Any circuit generating an output voltage
Radar transmitter
Amplifier
Computer terminal

## Slide 5: Why Need Transmission Line Theory
The key difference between circuit theory and transmission line theory is electrical size
For traditional circuit theory, the physical dimension of the circuit is much smaller than the wavelength
For transmission line theory, the physical dimension of the circuit is a considerable fraction of a wavelength, or many wavelengths
Ordinary Circuit
Transmission Line
λ
λ
Lumped system V and I roughly do not vary
Distributed system V and I vary in mag and phase

## Slide 6: Transmission Line Effects
Is the pair of wires connecting the voltage source to the RC load a transmission line? Yes.
The wires were ignored in circuits courses. Can we always ignore them? Not always.
Delayed by l/c
At t = 0, and for f = 1 kHz , if:
(1) l = 5 cm:
(2) But if l = 20 km:
λ = 300 km
Telephone cable

## Slide 7: Types of Transmission Modes
TEM Lines
Non-TEM Lines
This chapter

## Slide 8: Example of TEM Mode: Coaxial
Electric Field E is radial
Magnetic Field H is circular
Propagation is into the page
Magnitude and direction of E, H, V, I vary periodically in time and along the transmission line

## Slide 9: Dispersion in Transmission Lines
Dispersion/Distortion: Phase velocity vary with frequency
Nature of materials (material dispersion)
Non-TEM waveguides (structure dispersion)

## Slide 10: Transmission Line Model
Two thick wires
Lumped element model

## Slide 11: Interpretation of Parameters
L’ is the total self-inductance of the two conductors
C’ is the capacitance due to the close proximity of the two conductors
R’ is the resistance due to the finite conductivity of the individual conductors
G’ is conductance due to dielectric loss in the material between the conductors
Ordinary Wire

## Slide 12
Expressions will be derived in later chapters

## Slide 13: Transmission-Line Equations
ac signals: use phasors
Telegrapher’s equations

## Slide 14: Derivation of Wave Equations
Combining the two equations leads to:
Second-order differential equation

## Slide 15: Solution of Wave Equations (cont.)
General solutions:
Using:
It follows that:
Determined by structure and material
See p. 58

## Slide 16: Solution of Wave Equations (cont.)
In general:
wave along +z
wave along –z

## Slide 17: Summary of Impedance
So far we have learned three different concepts of impedance: wave impedance, intrinsic impedance and characteristic impedance
Wave Impedance
Wave
Intrinsic Impedance
Medium
Characteristic Impedance
Transmission Line
Feature of particular type of wave
Depends on material parameters
Ratio of voltage to current on a TL
For TEM waves, the wave impedance is equal to the intrinsic impedance. For example, plane wave and waves in a coaxial cable

## Slide 18: Example 2-1: Air Line

## Slide 19: Lossless Microstrip Line
Phase velocity in dielectric:
Phase velocity for microstrip:
Quasi-TEM

## Slide 20: Microstrip (cont.)

## Slide 21: Lossless Transmission Line
If
Then:
TEM

## Slide 23: Voltage Reflection Coefficient
At the load (z = 0):
Reflection coefficient
Normalized load impedance

## Slide 24: Voltage Reflection Coefficient

## Slide 25: Current Reflection Coefficient

## Slide 27: Standing Waves
voltage magnitude
current magnitude

## Slide 28: Standing-Wave Pattern
When voltage is a maximum, current is a minimum, and vice versa

## Slide 29: Standing Wave Patterns for 3 Types of Loads

## Slide 30: Maxima & Minima
Standing-Wave Pattern

## Slide 31: Maxima & Minima (cont.)
Voltage Standing Wave Ratio
For a matched load: S = 1
For a short, open, or purely reactive load:

## Slide 32: Example 2-6: Measuring ZL with a Slotted Line
See p. 74

## Slide 33: Wave Impedance
At a distance d from the load:

## Slide 34: Input Impedance
At input, d = l:
See p. 76

## Slide 35
Cont.

## Slide 36
(cont.)
Cont.

## Slide 37
(cont.)

## Slide 38: Short-Circuited Line
For the short-circuited line:
At its input, the line appears like an inductor or a capacitor depending on the sign of

## Slide 40: Open-Circuited Line

## Slide 41: Short-Circuit/Open-Circuit Method
For a line of known length l, measurements of its input impedance, one when terminated in a short and another when terminated in an open, can be used to find its characteristic impedance Z0 and electrical length

## Slide 42: Half Wavelength Line
So adding a half-wavelength transmission line does not change the load impedance
ZL
l
Z0
ZL
l+λ/2
Z0
Zin
Zin

## Slide 43: Quarter Wavelength Line
So adding a quarter-wavelength transmission line transforms the load impedance in an inverse manner
Useful in impedance matching since the reflection coefficient is 0

## Slide 44: Terminated by Another TL
Infinitely long or matched
Z1
Insertion loss (IL)

## Slide 47: Instantaneous Power Flow

## Slide 48: Average Power

## Slide 49: The Smith Chart
Developed in 1939 by P. W. Smith as a graphical tool to analyze and design transmission-line circuits
Today, it is used to characterize the performance of microwave circuits

## Slide 50: Complex Γ Plane
Γ = 0
Matching Point

## Slide 51: Constant SWR Circles
A circle with a radius of |Γ| is called SWR circle, since |Γ| is constant on this circle
|Γ| = 0.5
|Γ| = 0.25
|Γ| = 0.75
Re (Γr)
Im (Γi)
|Γ| = 1
SWR = 1.67
SWR = 3
SWR = 7
SWR = ∞

## Slide 52: Smith Chart Parametric Equations
Equation for a circle
The most usefulness of the Smith chart is converting from reflection coefficient Γ to normalized impedance zL
is constant on a specific circle
is constant on a specific circle

## Slide 53: Resistance (rL) Circles
Circles in the (Γr, Γi) plane centered at (,0) with a radius of and all pass through the point Γ = 1
centered at (0,0), radius is 1
the Big circle
big
small
o.c.
As increases, the center moves to the right and radius becomes smaller
centered at (1,0), radius is 0
a point at (1,0)

## Slide 54: Examples
rL circles are contained inside the unit circle

## Slide 55: Reactance (xL) Circles (Inductive)
Circles in the (Γr, Γi) plane centered at (, ) with a radius of
and all pass through the point Γ = 1
centered at (1,∞), radius is ∞ the horizontal line
inductive
+ big
+ small
centered at (1,0), radius is 0
a point at (1,0)
As increases, the center moves down and radius becomes smaller

## Slide 56: Reactance (xL) Circles (Capacitive)
centered at (1,∞), radius is ∞, the horizontal line
big
small
Circles in the (Γr, Γi) plane centered at (, ) with a radius of
and all pass through the point Γ = 1
capacitive
As decreases, the center moves down and radius becomes smaller
centered at (1,0), radius is 0
a point at (1,0)

## Slide 57: Examples
Only parts of the xL circles are contained within the unit circle

## Slide 58: rL and xL Circles
Given Γ = Γr + jΓi, zL = rL + jxL can be determined and vice versa
Every point in the Smith chart corresponds to a Γ and zL
When use the Smith chart to solve problems, Z0 is known and fixed
s.c.

## Slide 59
Complete Smith Chart
rL Circles
Positive xL Circles
Negative xL Circles

## Slide 60: Determine Input Impedance
ZL
Z0
Zin
Z0
Γe−2jβl
Γ
Same form
l
Normalized input impedance

## Slide 61: Determine Input Impedance (cont.)
Γ, zL
2βl
Γe−2jβl, zin
If zin is given, do a rotation counter-clockwise for an angle of 2βl will find the zL point
Same form
Re (Γr)
Im (Γi)
Rotating clockwise for one circle means adding a λ/2 line

## Slide 62: A Simple Way to Get SWR
Same
SWR can be obtained by drawing a SWR circle and get the intersection at the negative horizontal axis. Then read the SWR scale below the Smith chart
There is another simple way to get SWR
For a real load
So SWR can also be obtained by drawing a SWR circle and read the resistor value of the intersection at the positive horizontal axis

## Slide 63: Vmax and Vmin Point
The locations with maximum voltage (Vmax) and minimum voltage (Vmin), which can also be found in the Smith chart
The length of transmission line from the load to the first Vmax point and the first Vmin point can be found by the SWR circle
2βlmax
2βlmin
2βlmax
2βlmin

## Slide 64: Summary of Special Points and lines
Matching Point (Γ = 0)
Open Circuit (Γ = 1)
Short Circuit (Γ = −1)
Pure Reactance Circle (|Γ| = 1, rL = 0)
Pure Resistance Line (Γ real)
Vmin Line
Vmax Line

## Slide 65: Summary of Scales
Resistor
Γ Angle
Inductor
Capacitor
TL Length
SWR

## Slide 66: General Steps
|Γ|
Γ
θ
rL
xL
zL
zin
2βl

## Slide 67: Example
0.106 λ
0.406 λ
A load impedance 40 + 70j Ω terminates a 100 Ω transmission line that is 0.3 λ long. Find the reflection coefficient at the load, the reflection coefficient at the input to the line, the input impedance, the standing wave ratio on the line, and the return loss

## Slide 68
(a)
(b)
(c)
(d)

## Slide 69
Given:
S = 3
Z0 = 50 Ω
first voltage min @ 5 cm from load
Distance between adjacent minima = 20 cm
Determine: ZL

## Slide 70: Determine Admittance from Impedance
The Smith chart can be used to find normalized admittance in a simple way
Numerically
Rotate zL by half circle and read the impedance value to get yL

## Slide 71: Admittance Circles (gL and bL)

## Slide 72: Impedance and Admittance Calculation
ZL
R
ZL
R
zL
zL
yL
ZL
L
zL
ZL
L
zL
yL
ZL
C
zL
ZL
C
zL
yL
yin
zin
zin
yin
zin
Z0 can be arbitrary

## Slide 73: Impedance Matching

## Slide 74: Matching Network
The network has to transform the real part of the load impedance from RL (at the load) to Z0 at MM’ in the figure and transform the reactive part from XL (at the load) to zero at MM’
To achieve these two transformations, the matching network must have at least two degrees of freedom, which means two adjustable parameters

## Slide 75: Benefits of Matching
Assume the generator is matched, matching the load can enable maximum power delivered to the load
Can improve signal-to-noise ratio of impedance matching sensitive components, such as antenna and low-noise amplifier
In a power distribution network such as an antenna array feed network, matching can reduce amplitude and phase errors

## Slide 76: Important Design Factors
Complexity The simplest design that satisfies the required specifications is generally preferable. A simpler matching network is usually cheaper, smaller, more reliable, and less lossy than a more complex design
Bandwidth Any type of matching network can ideally give a perfect match at a single frequency. But it is desirable to match a load over a band of frequencies
Implementation Depending on the type of transmission line or waveguide being used, one type of matching network may be preferable to another
Adjustability In some applications the matching network may require adjustment to match a variable load impedance

## Slide 77: Possibility of Matching
So long as the load impedance ZL has a positive real part, a matching network can always be found

## Slide 78: Examples of Matching Networks

## Slide 79: Lumped-Element Matching
This type of matching technique uses lumped elements, like inductors and capacitors. Transmission lines can also be used
No resistors are used because of the loss they will induce

## Slide 80: L-section
L-section is the simplest type of matching network, which uses two reactive elements to match an arbitrary load impedance to a transmission line
Two possible configurations are shown below
zL inside the grey region
What about zL is on the 1 + jx circle?
zL inside the grey region

## Slide 81: Cont.
The jX and jB can be either inductors or capacitors
So there are in total eight possibilities for the L-section matching network
If the frequency is low enough and/or the circuit size is small enough, actual lumped-element capacitors and inductors can be used. This may be feasible for frequencies up to about 1 GHz. But in a large range of frequencies and circuit sizes, lumped elements may not be realizable. This is a limitation of the L-section matching network

## Slide 82: Analytical Solutions (First Kind)
Impedance-matching condition requires
Separating into real and imaginary parts gives
The solutions are
Two possible solutions Positive X is an inductor and negative X is a capacitor Positive B is a capacitor and negative B is an inductor

## Slide 83: Analytical Solutions (Second Kind)
Impedance-matching condition requires
Separating into real and imaginary parts gives
The solutions are
Still two possible solutions

## Slide 84: Smith Chart Solution (First Kind)
zL
yL
Get yL from zL
Rotate on a constant r circle (here also viewed as a constant g circle) to arrive at y1 on the symmetry of the r = 1 circle
Convert back to z1, which will be on the r = 1 circle
Rotate on the r = 1 circle to the matching point
y1
z1
jb
z1, y1
jx
Two possible solutions

## Slide 85: Smith Chart Solution (Second Kind)
zL
Rotate on a constant r circle to arrive at z1 on the symmetry of the r = 1 circle
Convert to y1, which will be on the r = 1 circle (here also viewed as the g = 1 circle)
Rotate on the r = 1 circle to the matching point
jx
y1
z1
jb
Two possible solutions

## Slide 86: Lumped-Element Matching with T-Lines
Choose d and Ys to achieve a match at MM’

## Slide 88: Cont.

## Slide 89: Single-Stub Matching
Replace the shunt element by a piece of short- or open-circuited transmission line

## Slide 91: Transients
Rectangular pulse is equivalent to the sum of two step functions

## Slide 92: Transient Response
Initial current and voltage
Reflection at the load
Second transient
Load reflection coefficient
Generator reflection coefficient

## Slide 93
T = l/up is the time it takes the wave to travel the full length of the line
Voltage Wave

## Slide 94
Current Wave
Reflection coefficient for current is the negative of that for voltage

## Slide 95: Steady State Response

## Slide 96
Bounce Diagrams

## Slide 98: Technology Brief 4: EM Cancer Zapper

## Slide 99: Technology Brief 4: High Voltage Pulses

## Slide 100: Summary