## Slide 1: 9. Radiation & Antennas
7e Applied EM by Ulaby and Ravaioli

## Slide 2: Overview
Introduction of Antenna Project
Radiation Mechanism (9-1)
Various types of antennas (9-1)
Hertzian Dipole (9-1)
Basic Antenna Radiation Characteristics (9-2)
Image Theory of Antenna
Half-wave Dipole and Monopole (9-3)
Friis Transmission Formula
Two-Element Array (9-9 and 9-10)
Summary

## Slide 3: Antenna Project
Task: to design a device that allows signal to be transmitted from the transmitter to the receiver
Objective: communication rate > 10 Mbits/s

## Slide 4: Antenna Specifications
A well-set two-antenna TX antenna system is shown in the figure. Students are to design their own antenna to replace the highlighted one.
Recommended antenna specifications: (also typical technical specifications for 2G base stations)
Center frequency: 3.6 GHz
Bandwidth: > 40 MHz
In-band |VSWR|: < 2
In-band Antenna Efficiency > 50 %
Radiation pattern: directional or omni-directional
Antenna type: monopole, dipole, spiral etc.
We are going to learn them now.

## Slide 5: Hertz’s Experiment: origin of antenna
High voltage on two wires → sparks in gap
EM travels through the air in certain direction
Sparks lead to EM waves leaving the wires
Another spark is created at the receiver and light up an LED

## Slide 6: Radiation Mechanism
Source of radiation:
accelerated charged particles.
(more details in the next page)
Question: How do EM fields leave from wires and propagate through a space? (radiation principle)
Radiating EM field
Radiating EM field

## Slide 7: Radiation Mechanism
Radiating EM field
E-field of static charge in a constant velocity (both speed and direction)
Accelerated charge creates a kink (discontinuity) between old field and new field
Old field
New field
acceleration

## Slide 8: Radiation Mechanism
Let a camera move at same speed with the charge (speed of light!). The kink propagates out.
Conclusion: acceleration of the charge has caused electromagnetic radiation

## Slide 9: Radiation Mechanism
Concept of Dipole : two oscillating charges

## Slide 10: Fields of Moving Charges
http://phet.colorado.edu/sims/radiating-charge/radiating-charge_en.html
A static charge produces static electric field at the speed of light
When a charge is moving, the generated electric fields change accordingly
When the charge moves with acceleration, the generated electric fields exhibit oscillating natures, which will in turn generate magnetic fields and form electromagnetic fields
A good resource

## Slide 11: TX: Wave from T-Line to Space
Antenna in transmitting mode
An antenna serves to radiate electromagnetic field

## Slide 12: Analogy to Capacitor
Use the analogy between a capacitor and an antenna to give an intuitive explanation of radiation
This analogy is based on the fact that the electric fields generates displacement currents that together with the conduction currents form a closed loop of the circuit
Capacitor
V
E
Antenna

## Slide 13: RX: Wave from Space to T-Line
Oscillating fields of waves induce positive and negative charges at the ends of the antenna. A varying voltage signal is produced at the center gap of the antenna, which propagates along the T-Line to the detector or receiver.
Antenna in RX mode
The same antenna serves to receive electromagnetic field

## Slide 14: Antenna Properties
1. An antenna is a transducer that converts efficiently a guided wave propagating on a transmission line into an electromagnetic wave propagating in an unbounded medium (usually free space), or vice versa.
2. Most antennas are reciprocal devices, exhibiting the same radiation pattern for transmission as for reception.
3. Being a reciprocal device, an antenna, when operating in the receiving mode, can extract from an incident wave only
that component of the wave whose electric field matches the antenna polarization state.

## Slide 15: Examples of Antennas

## Slide 16: Example of Monopole Antenna
L
Conducting Plate
SMA connector, antenna input port
Conducting wire
W
Project:
You can tune the length L and ground width W for maximum antenna efficiency in 3.6-GHz band, by hands or by simulation first.

## Slide 17: General Circuit-Model of Antennas
Rrad : radiation resistance, scalar, a measurement of how much power is radiated to the whole space. (related to antenna design，e.g., antenna length)
Rloss : loss resistance, scalar, a measurement of how much power is converted to heat due to finite conductivity of conducting materials (σ) and dielectric loss (μ’’and ε’’). (related to material and antenna design)
XA : antenna reactance, scalar, a measurement of how much power is restored inside the antenna. (related to material and antenna design）
Antenna Impedance ZA
Input impedance of the antenna when looking toward the load, at A-A’，complex in general
Zg
ZA
Z0，βl
Z0，βl
Due to reciprocity, TX mode is assumed from now on, unless otherwise specified.
A
A’
ZA = Rrad + Rloss + jXA
ZA

## Slide 18: Far-Field Approximation
1. In close proximity to a radiating source, the wave is spherical in shape, but at a far distance, it becomes approximately a plane wave as seen by a receiving antenna.
2. The far-field approximation simplifies the math.
3. The distance beyond which the far-field approximation is valid is called the far-field range (will be defined later).
Most antenna characteristics are defined and discussed in the Far-Zone only.

## Slide 19: The Hertzian Dipole
Definition: A Hertzian dipole is a thin, linear conductor whose length l is very short compared with the wavelength λ. l < λ/50.
Current distribution: this restriction allows us to treat the current along the length of the conductor as constant, even though it has to decay to zero at the ends of the wire.
The field of the entire antenna may be obtained by integrating
the fields from all these differential antennas, with the proper
magnitudes and phases taken into account
z
Amplitude of current
I0

## Slide 20: Current Distribution on Wires
The wave traveling between the wires undergoes a total reflection at the end of the wire and forms standing wave on the wires
The current at the end of the wires are always zero

## Slide 21: Current and Voltage Distribution
z
Amplitude of current
I0
When antenna length is very, very, very small, the current distribution goes to uniform. (Hertzian dipole)
Field radiated ？
Half wave

## Slide 22: Fields Radiated by Hertzian Dipole
1. Current distribution along a Heartizian dipole:
Time varying
Phasor form
(constant)
2. E-field and H-field produced
is the intrinsic impedance of free space.

## Slide 23: Radiated Electric Field
Completed form
What we are interested ？
Fields at a distance of R far from the source

## Slide 24: Fields Radiated by Hertzian Dipole (cont.)
Completed form
Far-field approximation
When kR >> 1, dominates the radiation
are neglected
though, they dominate the near-field

## Slide 25: Hertzian Dipole—Far-Field Approximation
At
Far-field of Hertzian dipole

## Slide 26: Hertzian Dipole—Far-Field Approximation
Antenna Polarization: polarization of the EM wave radiated by the antenna in a given direction
Far-field of Hertzian dipole
Importance:
If there is no reflection from environment (multi-path propagation), the TX antenna and RX antenna must be in the same polarization for maximum transmission, which will be seen later in the Friss Equation.
If there are multiple reflections, an optimum polarization may be found by channel estimation.
Polarization of Hertzian dipole

## Slide 27: Antenna Radiation Characteristics
Radiation Intensity
Radiation Pattern
Half-Power Beamwidth
Antenna Directivity
Radiation Efficiency
Antenna Efficiency
Antenna Gain
Bandwidth

## Slide 28: Normalized Radiation Intensity
Electric and Magnetic Fields
Average Power Density (W/m2)
Normalized Radiation Intensity
W/m2
Where the radiated energy goes ？
When θ=90°
Proportional to |I0|2 and (l/ λ)2

## Slide 29: Radiation Pattern of Hertzian Dipole
Normalized Radiation Pattern
Careful, ratio of power, not field

## Slide 30: 3D Radiation Pattern of A Dipole
Radiation Pattern:
Far-field properties
A function of direction (θ，φ)
A dimensionless quantity
Describes the ability of antenna to collect power from or radiate power toward a specified direction.
By virtue of reciprocity, a receiving antenna has the same directional antenna pattern as the pattern that it exhibits when operated in the transmission mode.

## Slide 31: Total Radiation Power (Prad)
A surface integral by math
2. Total Radiated Power
Differential area
Solid Angle
Power radiated through dA
Total Radiated Power

## Slide 32: Example of 3-D Pattern
F (dB) = 10 log F
Principal planes:
1. Elevation plane (x-z and y-z planes)
2. Azimuth plane (x-y plane)
Not 20 as it is defined by ratio of power, rather than field intensity

## Slide 33: Different Pattern in Different Scale
Not a dipole, but another antenna

## Slide 34: Polar and Rectangular Plots

## Slide 35: Beamwidth
Half-power beamwidth (HPBW)
Since 0.5 corresponds to ‒3 dB, the half power beamwidth is also called the 3-dB beamwidth.
IMPORTANT

## Slide 36: Pattern Solid Angle
See p. 412
Equivalent Solid Angle
steradian

## Slide 37: Antenna Directivity D
Antenna pattern solid angle
Directivity
Maximum normalized radiation intensity = 1
Average value of F(θ,φ) over all directions

## Slide 38
Cont.

## Slide 39
(cont.)

## Slide 40
IMPORTANT

## Slide 41: Radiation Efficiency and Gain
Radiation efficiency
Antenna gain G
Radiation efficiency does not consider impedance mismatch
IMPORTANT

## Slide 42: Antenna Radiation and Loss Resistances
Antenna is merely a load with input impedance Zin
IMPORTANT

## Slide 43
Cont.

## Slide 44: Example 9-3 (cont.)
For any antenna:
For the Hertzian dipole:
IMPORTANT

## Slide 45: Antenna Bandwidth
Gain Flatness < 1dB
Ant. Eff. > 75%
HPBW
Definition
The frequency range within which all requirements of antenna characteristics are satisfied simultaneously.
Example
A base-station antenna for mobile communication has the following technical specifications.
Specification | Test Results | Bandwidth
VSWR | <1.5 | 3.2 – 3.8 GHz
Antenna Efficiency | > 75% | 3.4 – 4.5 GHz
HPBW | 120°±5° | 3.4 – 4.2 GHz
Gain flatness | < 1dB | 3.3 – 4.6 GHz
Cross-polarization level | < -20 dB | 1.5 – 12 GHz
Bandwidth: 3.4 – 3.8 GHz
Freq. (GHz)
DC
VSWR<1.5
X-pol
REQUIREMENT: given antenna characteristics to determine required bandwidth

## Slide 46: Image Theory
Motivation
The radiation of antennas are determined by source and boundaries. Therefore, it matters where an antenna is mounted on or what exists nearby.
Example
A segment of conducting copper wire that carries oscillating currents
Case I: the current is vertically placed above an infinitely large PEC plate.
PEC plate
Conducting wire
Feeding gap
(voltage source)
Electric currents
Simplified model Arrow shows direction of current flow
Electric
currents
To be continued.
Definition
The effect of a boundary on antenna far field can be replaced by a virtual source
IMPORTANT

## Slide 47: Image Theory (monopole)
Motivation
The far-field radiation characteristics of antennas are determined by source and boundaries. Therefore, it matters where an antenna is mounted on or what exists nearby.
Example
A segment of conducting copper wire that carries oscillating currents
A segment of current vertically placed above an infinitely large PEC plate.
From original problem to equivalent problem
Original
+
-
–
+
+
–
Equivalent for upper space ONLY
Zero field for lower-half space
An image current of same orientation is placed below the ground, as if the total field IN THE ORIGINAL SPACE was produced by both currents without the ground. However, ZERO is the field in the lower half space. (effect of ground is replaced by image source). Textbook pp. 420 and Figure 9-15.

## Slide 48: Image Theory (monopole)
Important characteristics of λ/4 monopole
Pattern of a λ/4 monopole looks like a λ/2 dipole for half space
The radiation is limited to upper half-space (0 ≤ θ ≤ π/2)
A monopole radiates only half as much power as the dipole
Prad = 18.3 I02 and Rrad = 36.5 Ω
A segment of conducting copper wire that carries oscillating currents
HINT:
simulation can answer the above questions
Questions
What may be a good length of the monopole of your antenna project?
What may be the width of the ground plane when infinite ground is impossible?(Effect of finite ground.)
Is it OK to have a length of Nλ/4 for the antenna project? For example, VSWR, antenna efficiency, input impedance, antenna matching and so on… (different resonant mode with different radiation pattern)

## Slide 49: Image Theory (general summary)
Image of electric and magnetic currents over infinite PEC plate
PEC
Electric currents
Magnetic currents
Image of electric and magnetic currents over infinite PMC plate
PMC
Electric currents
Magnetic currents
REQUIREMENT: sketch the image of a given source and boundary.

## Slide 50: Half-Wave Dipole
2. For Hertzian dipole of length l, E field is:
1. Current in half-wave dipole （phasor）
3. Each length element dz of half-wave dipole is like a Hertzian dipole, radiating a field
4. For the entire dipole, the total radiated field is
See p. 418
Now we calculate the field of λ/4 monopole by looking at λ/2 dipole
Field summation theorem
Derivation not required

## Slide 51: Half-Wave Dipole (cont.)
Integration leads to:

## Slide 52: Radiation Pattern of Half-Wave Dipole
Radiation pattern resembles that of the Hertzian dipole. Its beamwidth is slightly narrower, 78 degrees compared with 90 degrees for the Hertzian dipole.
REQUIREMENT: given a radiation pattern in terms of mathematical function, to sketch the shape of the radiation pattern in a given plane.

## Slide 53: Other Half-Wave Dipole Properties
1. Directivity
Numerical integration gives:
2. Radiation Resistance
This is very important, because it makes it easy to match the antenna to a 75-Ω transmission line. In contrast, the radiation resistance of a dipole whose length is much shorter than a wavelength is on the order of 1 Ω or less.

## Slide 54: Dipole of Arbitrary Length
Length of dipole controls the radiation pattern by controlling the current distribution over the wire. (because field is a result of source and boundary)
OPTIONAL

## Slide 55: Radiation Pattern of Different Dipole
OPTIONAL
The pattern helps answer an earlier question about the length of the monopole, do you remember?

## Slide 56: Friis Transmission Formula
IMPORTANT
Motivation
How much power is received by a receiving antenna?
How to improve the receiving power?
RX pattern
TX pattern
Spherical factor
[4π(R/λ)]-2
TX gain
RX gain
Prec is direction dependent
pp. 427–428

## Slide 57: Two-Element Antenna Array
Major Motivation
To increase antenna gain and directivity.
To shape the radiation pattern so energy & signal can be delivered to required direction.
To generate multiple beams.
To filter out undesired noise from certain directions
To combine EM power in space (rather than in circuit for guided waves)
To control reflected wave （reflectarray）
Definition:
An array of antenna elements (identical or different) fed by a combination of weighted signals, from guided-wave network or space, for a desired summation of total field. For example, beam steering, energy focus, holography, beam switching etc.

## Slide 58: Two-Element Antenna Array
An antenna array to a continuous aperture is analogous to digital data to analog. By controlling the signals fed into individual array elements, the pattern can be shaped to suit the desired application.
Also, through the use of electronically controlled solid-state
phase shifters, the beam direction of the antenna array can
be steered electronically by controlling the relative phases
of the array elements.
This flexibility of the array antenna has led to numerous
applications, including electronic steering and multiple-beam
generation.

## Slide 59: Two-Element Antenna Array
Example
Given the far-field of a z-oriented Hertzian dipole
An additional Hertzian dipole of identical current magnitude is further added at the origin but oriented along x-axis.
Determine the total field at a distance of R, in the direction of θ = φ = π/2,. State the polarization of the total field in the direction
x
y
z
Key is field summation theorem

## Slide 60: Summary
Introduction of Antenna Project
  Due in 17 days : Simulation, fabrication, testing and writing.
Radiation Mechanism
  Deep understanding of radiation mechanism: acceleration
Basic Principles
  Field summation theorem
  Image theory: point charge, electric/magnetic currents, PEC/PMC
  Far-field approximation
Hertzian Dipole
  Current, field, pattern and polarization
Coordinate System

## Slide 61: Summary
Basic Antenna Radiation Characteristics
  Radiation intensity and radiation pattern
  Concepts of Reciprocity, Polarization, pattern, two efficiencies, directivity, gain, HPBW, bandwidth
  Circuit model and antenna impedance: physical meaning of Rrad, Rloss, reactance and controlling factors.
Half-wave Dipole
  Current, field, pattern and polarization
Friis Transmission Formula
  Clear understanding of each parameter for calculation of power delievery
Two-Element Array
  Field summation theorem is the key